Lamine Hafiane / 04.11.21
* monitoring of the control signals with an oscilloscope via MULTI-IO :
* Test without chip
* ADC_DATA is connected to CLK_CMP (FPGA → LVDS → LVDS → FPGA)

N	FPGA_OUT	Signals (FPGA)	Oscilloscope connector
0	MULTI_IO[0]	CLK_CMP	D0
1	MULTI_IO[1]	CLK_SR	D1
2	MULTI_IO[2]	SAMPLE	D2
3	MULTI_IO[3]	RST_B	D3
4	MULTI_IO[4]	RX_EN	D4
5	MULTI_IO[5]	ADC_DATA	D5
6	MULTI_IO[6]	CLK_SPI	D6
7	MULTI_IO[7]	LCK_BUF (main clk)	D7

Figure	Description
adc1M_000	Sampling frequency (Fs) : 1 MHz | CLK_CMP is used here to emulate the ADC input : 10101010101
adc1M_001	The same as adc1M_000. Measure the delay between CMP_CLK and ADC_DAT (FPGA → LVDS → LVDS → FPGA) | Delat_t ~ 11ns
adc1M_002	The same as adc1M_000. Measure the time reserve (Zeitpuffer) for the bit readout (because there will be an additional delay through the ASIC)! | at Fs=1MHz we have a margin of ~35ns!
adc1M-normal-cmp-clk_000	The same as adc1M_000 | shows the actual control signals (CLK_CMP is not used here to emulate the ADC output)
adc1M-normal-cmp-clk_000	The same as adc1M-normal-cmp-clk_000.
adc2M5_002	The same as adc1M_000 but Sampling frequency (Fs) : 2.5 MHz